Activity 5: Assessment report of the toxic substances on the small lake sediments

Trilateral cooperation on Environmental Challenges in the Joint Border Area

Vladimir A. Dauvalter

Institute of North Industrial Ecology Problems, Kola Science Center, RAS

This publication has been produced with the assistance of the European Union, but the contents of this publication can in no way be taken to reflect the views of the European Union.

Introduction

The border area between Russia, Norway, and Finland is exposed to serious industrial impact, including that by the Pechenganikel integrated plant. Lake Kuetsjarvi and the lower watercourse of the Pasvik River receive wastewater from smelting and by-processes located in the settlement of Nikel. The whole system of the Pasvik River as well as lakes and rivers of this area not belonging to the system are exposed to pollution via atmospheric depositions. The major pollutants include compounds of sulfur and heavy metals (HM’s) – Ni, Cu, Cd, Cr, Zn, As, Hg, etc., polycyclic aromatic hydrocarbons (PAH’s), and persistant organic pollutants (POP’s). Sulfur dioxide emissions from the intergrated plant result in acidification of the surface water and its pollution due to intensification of rock desalination processes.

# Industrial development of copper-and-nickel ore deposits was started in 1932 by a joint Canadian-Finnish company (after the October Revolution the today’s territory of Pechenga region belonged to Finland and after the war between the USSR and Finland in 1939-1940 it was annexed by the USSR). The Pechenganikel integrated plant has been in operation since 1946 when processing of the local sulfide-and-nickel ore was resumed in the settlement of Nikel. In 1959 ore extraction at Zhdanovskoye Field and its processing in the town of Zapoliarny began. The combine plant’s emissions include sulfaric gas, Ni, Cu, other HM’s, dust, as well as nitrogen oxides and carbon oxides from boiler houses.

# Materials and methods

For the study of ecological status of the lakes in the border area between Russia, Norway, and Finland columns of bottom sediments (BS) were sampled from 16 lakes (Fig.1): 4 lakes in Finland: 1 – Lampi 222 , 2 – Harrijärvi, 3 – Pitkä-Surnujärvi, 4 – Sierramjärvi, 8 lakes in Russia: 5 – Pikkujarvi, 6 – Shuonijaur, 7 – Ila-Nautsijarvi, 8 – Ala-Nautsijarvi, 9 – Toartesjaur, 10 –Virtuovoshjaur, 11 – Riuttikjaure, 12 – Kochejaur, and 4 lakes in Norway: 13 – Gardsjøen, 14 – Holmvatnet, 15 – Rabbvatnet, 16 – Durvatn.

The BS columns were sampled in the deepest areas of the water bodies under study by an open gravity type column sampler (internal diameter 44mm) with automatically closing diaphragm. The sampler is made of plexiglass by template desined by Skogheim (Skogheim, 1979) to transport the columns intact for further use. The BS columns were 15 to 45cm long depending on the conditions of their formation and their physical-and-chemical properties. The BS columns were divided into 1sm layers (in specific cases 0.5cm), placed in polyethelene containers and sent to laboratory for analysis where they were stored at a temperature 4(С until analyzed.

Fig.1. Location of the lakes under study (2012-2013) – Finnish lakes: 1 – Lampi 222, 2 – Harrijärvi, 3 – Pitkä-Surnujärvi, 4 – Sierramjärvi; Russian lakes: 5 – Pikkujarvi, 6 – Shuonijaur, 7 – Ila-Nautsijarvi, 8 – Ala-Nautsijarvi, 9 – Toartesjaur, 10 –Virtuovoshjaur, 11 – Riuttikjaure, 12 – Kochejaur; Norwegian lakes: 13 – Gardsjøen, 14 – Holmvatnet, 15 – Rabbvatnet, 16 – Durvatn.

The primary treatment of the BS samples (drying, humidity measurement, ignition, and measurement of loss during ignition) and measurement of elements content (Ni, Cu, Co, Zn, Cd, Pb, Hg, Mn, Fe, Ca, Mg, Na, K, Al, Cr, P, and Sr) was performed in the laboratories of Institute of North Industrial Ecology Problems (INEP), Kola Science Center, RAS, Apatity, Russia, and the Norwegian Institute of Water Research (NIVA), Oslo, Norway.

The samples (ca. 5g) were dried in a drying box under a temperature 105ºС for 6 h, and sample humidity was determined. (Håkanson, 1984). Then the samples were baked in a muffle furnace at a temperature 450-500ºС for 4 h in order to determine the loss on ignition (LOI) as indirect indicator of organic matter content. Then, the samples were milled in a jasper mortar and kept under a temperature 4ºС before chemical analysis.

To determine the gross metal concentrations 0.3g sample weight was treated with 3ml concentrated nitric acid (HNO3) of ultra high purity class in autoclave with a teflon insert at a temperature 140ºС for 5 h. The autoclave content was then cooled down to room temperature and 2.5 ml aliquot was placed into a 60 ml plastic bottle and diluted with deionized water up to volume 25 ml.

The resultant BS solutions were analyzed by atomic absorption spectrophotometer AAS-30 in the flame acetylene-air (Cr, Co, Fe, and Mn), in the flame acetylene-nitrogen monoxide (Sr and Al); Perkin-Elmer-360) in the flame acetylene-air (Ni, Cu, and Zn), in the flame propane-butane-nitrogen monoxide (Ca and Mg), in the flame propane-air (Na and K). Concentrations of Cd, Pb, and As were determined with the device AAN-800 (electrothermal atomization). Concentrations of Hg were determined by way of cold steam atomic absorption with the help of Perkin-Elmer FIMS 100 device. Quality control was performed by analysis of standard samples PACS-2 (Canada) and L6M (Finland). The deviations from standardized values did not exceed the acceptable error for the elements under study (20-25%). All the metal concentrations are given in microgram per gram (µg/g) of dry weight.

The level of industrial load on the lakes’ ecosystems was determined according to the estimated pollution factor (Cf) for each of the priority HM contaminant (Ni, Cu, Co, Zn, Pb, Cd, Hg, and As). The Cf value was found by dividing HM concentration in the surface (present-day) layer )0-1cm) by its background content in the deepest layer formed in the pre-industrial period (Håkanson, 1980,). The BS contamination degree (Cd) was determined by the sum of all Cf values for the eight HM in a particular lake.

# Background concentrations of elements in bottom sediments

The study of background HM concentrations in the BS is one of the central issues in the study of lakes pollution. Samples of BS taken from the deepest layers of the columns (usually, over 20cm) allow finding background HM concentrations in the course of lakes pollution study. According to earlier studies (Norton et al., 1992, 1996; Rognerud et al., 1993), these layers were formed over two hundred years ago, i.e. before industrial development of North Fennoscandia. The background HM concentrations reflect the geo-chemical peculiarities of the catchment area, provide information about quantitative values of water bodies’ pollution degree, and help determine anomalies for the purpose of mineral resources exploration (Tenhola, Lummaa, 1979).

The background HM concentrations in BS of the lakes under study are fairly volatile which reflects considerable variations in the catchment area geochemistry (bedrock and quaternary rock, and soils covering them), the erosion processes rate, drainage module (water, ion, and solid matter), i.e. all conditions of formation of the lakes’ BS chemical composition.

The maximum background HM concentrations in BS (Table 1) were found in different lakes: Cu and Hg in Lake Lampi 222, Zn and Cd in Lake Ala-Nautsijarvi, Co in Lake Ila-Nautsijarvi, Ni in Lake Pikkujarvi, Pb in Lake Holmvatnet, and As in Lake Gardsjøen, which is accounted for by the geochemical and morphometrical peculiarities of the catchment area and the lake itself, as it was noted above. For example, in the catchment areas of Lakes Pikkujarvi, Ala-Nautsijarvi and Ila-Nautsijarvi copper-and-nickel sulfide deposites are represented by such minerals as pentlandite (Fe,Ni)9S8, copper pyrite CuFeS2, white cobalt (Co,Ni)AsS, nicolite NiAs and others (Gregurek et al., 1999), which explains the fairly high concentrations of almost all HM in the BS background layers of the lakes under study.

Table 1. Background concentrations (µg/g of dry weight) of elements in BS of the lakes under study.

Average* – average background concentrations in BS in the North-West of Murmansk Region and border areas of the neighboring countries (Kashulin et al., 2009).

| Lakes | Layer, cm | LOI | Cu | Ni | Zn | Cd | Co | Pb | As | Hg |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Lampi 222 | 29-30 | 31.30 | 200 | 21 | 145 | 0.54 | 11 | 7.0 | 1.9 | 0.318 |
| Harrijärvi | 29-30 | 24.24 | 24 | 16 | 123 | 0.20 | 4 | 6.9 | 1.7 | 0.046 |
| Pitkä-Surnujärvi | 29-30 | 17.91 | 64 | 20 | 98 | 0.45 | 9 | 4.4 | 1.8 | 0.068 |
| Sierramjärvi | 29-30 | 18.51 | 18 | 26 | 83 | 0.25 | 7 | 4.8 | 1.8 | 0.032 |
| Shuonijaur | 15-16 | 33.03 | 23 | 27 | 73 | 0.16 | 7 | 2.8 | 1.6 | 0.064 |
| Ala-Nautsijarvi | 24-25 | 27.24 | 58 | 75 | 254 | 1.06 | 43 | 12.5 | 4.6 | 0.178 |
| Ila-Nautsijarvi | 14-15 | 29.32 | 18 | 35 | 169 | 0.29 | 13 | 2.3 | 2.6 | 0.048 |
| Pikkujarvi | 13-14 | 20.8 | 59 | 78 | 96 | 0.13 | 11 | 5.8 | 2.6 | 0.056 |
| Toartesjaur | 22-23 | 30.21 | 13 | 19 | 63 | 0.11 | 8 | 1.5 | 1.6 | 0.042 |
| Virtuovoshjaur | 14-15 | 52.51 | 14 | 36 | 100 | 0.23 | 14 | 8.2 | 2.1 | 0.088 |
| Riuttikjaure | 16-17 | 25.1 | 15 | 29 | 90 | 0.19 | 5 | 3.1 | 1.4 | 0.010 |
| Kochejaur | 17-18 | 37.8 | 17 | 27 | 100 | 0.17 | 11 | 3.7 | 1.7 | 0.092 |
| Gardsjøen | 29-30 | 34.85 | 69 | 41 | 86 | 0.47 | 14 | 3.6 | 5.4 | 0.108 |
| Holmvatnet | 29-30 | 23.92 | 79 | 41 | 178 | 0.82 | 31 | 26.1 | 3.8 | 0.100 |
| Rabbvatnet | 42-43 | 32.40 | 76 | 24 | 106 | 0.21 | 5 | 3.1 | 3.1 | 0.078 |
| Durvatn | 29-30 | 31.15 | 31 | 22 | 59 | 0.34 | 30 | 2.9 | 5.1 | 0.062 |
| Average |  | 29.39 | 49 | 34 | 114 | 0.35 | 14 | 6.2 | 2.7 | 0.087 |
| Median |  | 29.77 | 28 | 27 | 99 | 0.24 | 11 | 4.0 | 2.0 | 0.066 |
| Mininun |  | 17.91 | 13 | 16 | 59 | 0.11 | 4 | 1.5 | 1.4 | 0.010 |
| Maximum |  | 52.51 | 200 | 78 | 254 | 1.06 | 43 | 26.1 | 5.4 | 0.318 |
| St.deviation |  | 8.44 | 47 | 18 | 51 | 0.27 | 11 | 6.0 | 1.3 | 0.073 |
| Average* |  |  | 33 | 41 | 96 | 0.17 | 16 | 3.2 | 4.6 | 0.040 |

| Lakes | Mn | Fe | P | K | Nа | Ca | Mg | Sr | Al |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Lampi 222 | 313 | 57714 | 2270 | 571 | 88 | 2815 | 1060 | 14 | 32573 |
| Harrijärvi | 77 | 67276 | 754 | 381 | 67 | 1630 | 526 | 15 | 13198 |
| Pitkä-Surnujärvi | 926 | 46190 | 1454 | 797 | 253 | 3221 | 2500 | 17 | 15331 |
| Sierramjärvi | 268 | 44444 | 2240 | 777 | 263 | 3171 | 1538 | 21 | 14152 |
| Shuonijaur | 157 | 16364 | 768 | 1429 | 343 | 4703 | 3810 | 21 | 13152 |
| Ala-Nautsijarvi | 1000 | 82837 | 2238 | 1702 | 179 | 3472 | 2526 | 37 | 23400 |
| Ila-Nautsijarvi | 406 | 46000 | 874 | 923 | 194 | 5185 | 2742 | 27 | 14929 |
| Pikkujarvi | 263 | 25333 | 528 | 4077 | 588 | 8552 | 8318 | 33 | 20812 |
| Toartesjaur | 118 | 7797 | 694 | 409 | 94 | 4524 | 1333 | 15 | 10127 |
| Virtuovoshjaur | 390 | 20597 | 798 | 1143 | 164 | 4054 | 2095 | 31 | 18429 |
| Riuttikjaure | 167 | 7742 | 720 | 1037 | 129 | 4202 | 2000 | 23 | 13583 |
| Kochejaur | 138 | 6498 | 448 | 337 | 127 | 5167 | 1029 | 48 | 11364 |
| Gardsjøen | 167 | 31579 | 2442 | 882 | 218 | 5000 | 2543 | 23 | 20867 |
| Holmvatnet | 908 | 44776 | 1944 | 1176 | 233 | 3724 | 3078 | 21 | 21178 |
| Rabbvatnet | 120 | 18000 | 1412 | 1600 | 352 | 4850 | 3810 | 28 | 16668 |
| Durvatn | 250 | 20000 | 1692 | 588 | 158 | 3378 | 1674 | 22 | 6931 |
| Average | 354 | 33947 | 1330 | 1114 | 216 | 4228 | 2536 | 25 | 16668 |
| Median | 256 | 28456 | 1143 | 903 | 187 | 4128 | 2298 | 22 | 15130 |
| Mininun | 77 | 6498 | 448 | 337 | 67 | 1630 | 526 | 14 | 6931 |
| Maximum | 1000 | 82837 | 2442 | 4077 | 588 | 8552 | 8318 | 48 | 32573 |
| St.deviation | 308 | 22699 | 714 | 894 | 130 | 1511 | 1810 | 9 | 6150 |

Generally, the average background HM concentrations in BS of the lakes under study (Table 1) are similar to the average background concentrations in water bodies of the North-West of Murmansk Region estimated earlier (Kashulin et al., 2009). Chalcophylic elements Cd, Pb and Hg make an exception with their background concentrations in BS of the lakes under study two times higher, and As – 2 times lower than established before (Kashulin et al., 2009). The discrepancies between the calculated values of average background HM concentrations may be associated with changes of the list of lakes for BS sampling in different years.

The concentrations of Hg in the background BS of the lakes under study stay within the range 0.010 to 0.318 µg/g, the average value being 0.087 µg/g. For comparison, Table 2 presents background Hg concentrations in BS of Fennoscandia and North America. Comparing the results, a conclusion may be made that the Hg background values in other author’s studies are consistent with our data (Table 2). The best consistence is observed with studies of Swedish and Finnish boreal lakes except for Lake Lampi 222 where the maximum Hg concentration was discovered in the background layers of BS.

Table 2. Background Hg values (µg/g of dry weight) in BS of lakes in Fennoscandia and North America.

| Country | Lake/Territory | Hg | Source |
| --- | --- | --- | --- |
| Norway | Lake Tirifjorden | 0.050 | Abry et al., 1982 |
| Norway | Lake Mjessa | 0.070-0.090 | Rognerud, 1985 |
| Sweden | Boreal lakes | 0.030-0.095 | Håkanson, Jansson, 1983 |
| Sweden | Boreal lakes | 0.050-0.120 | Johansson, 1988 |
| Finland | Boreal lakes | 0.020-0.050 | Rekolainen et al., 1986 |
| The US | Wisconsin | 0.040-0.070 | Rada et al., 1989 |
| The US | North Minnesota | 0.030-0.060 | Megar, 1986 |
| Canada | Ontario | 0.100 | Douglas, 1986 |
| The US/Canada | The Great Lakes | 0.030-0.080 | Mudroch et al., 1988 |

The concentration of elements in BS depends on morphometrical parameters and a number of geological, geochemical, physical, chemical, and biological factors of the lakes (Strakhov et al., 1954). To identify the factors having the greatest impact on the chemical composition formation of the lakes’ BS factor analysis was performed (Table 3) which determined the first factor of the largest weight (27%) comprising the HM contained in higher concentrations in the bedrock and Quarternary rock in the North-West of Murmansk Region and border area – Zn, Co, Cd, as well as elements which behaviour depends on physical and chemical conditions in the BS and water column (primarily, the redox potential) and the lake’s trophic status – Fe, Mn, and P. Other HM under study – Cu, Ni, Pb, As, and Hg – have fairly high coefficients in this factor, which confirms the relation between practically all the HM under study. The first thing in common is presence of HM deposits in sulfide minerals in the territory under study which was noted before (Gregurek et al., 1999). Alkaline and alkaline-earth metals (K, Na, Ca, Mg), have the highest coefficients in the second factor; these are the major rock-forming metals in the bedding magmatic and metamorphic rocks constituting the lakes catchment area. This confirms the influence by bedrock geochemical composition on the formation of the BS background layers chemical composition. The absolute elevation of the lake water line has a high negative coefficient in this factor, i.e. the elements’ content in the background BS layers decreases when the elevation above the sea level increases. Humidity as a physical factor also has an impact on the BS chemistry, which is reflected by the high coefficient of this indicator in the third factor.

Table 3. Factor model of chemical composition of the BS background layers in the lakes under study. The most important parameters with coefficients over 0.7 are highlighted in bold.

|  | Factor 1 | Factor 2 | Factor 3 |
| --- | --- | --- | --- |
| Layer | 0.359 | -0.397 | -0.500 |
| Catchment | 0.203 | 0.184 | 0.510 |
| area | -0.343 | 0.082 | 0.566 |
| masl | -0.193 | -0.726 | 0.092 |
| Distance | -0.293 | -0.515 | 0.414 |
| H2O | -0.251 | -0.181 | 0.754 |
| LOI | -0.246 | -0.084 | 0.398 |
| Cu | 0.641 | -0.108 | -0.492 |
| Ni | 0.507 | 0.707 | 0.352 |
| Zn | 0.772 | -0.045 | 0.443 |
| Co | 0.722 | -0.009 | 0.503 |
| Cd | 0.927 | -0.186 | 0.264 |
| Pb | 0.692 | -0.040 | 0.176 |
| As | 0.571 | 0.104 | 0.144 |
| Hg | 0.642 | -0.242 | -0.065 |
| Mn | 0.752 | -0.020 | 0.233 |
| Fe | 0.750 | -0.262 | 0.048 |
| P | 0.732 | -0.355 | -0.219 |
| K | 0.229 | 0.928 | -0.096 |
| Nа | 0.088 | 0.889 | -0.275 |
| Ca | -0.183 | 0.905 | 0.040 |
| Mg | 0.151 | 0.962 | -0.185 |
| Sr | -0.032 | 0.432 | 0.704 |
| Al | 0.523 | 0.072 | -0.429 |
| Factor weight, % | 26.9 | 22.6 | 14.9 |

Cluster analysis (Fig.2) clearly identified three groups of water bodies: the first group includes Finnish lakes (Pitkä-Surnujärvi and Sierramjärvi) and a similar Russian lake Ila-Nautsijarvi, the second group includes the Russian lakes (Shuonijaur and Virtuovoshjaur) and the Norwegian lake Rabbvatnet, and the third group includes the Russian lakes Toartesjaur, Kochejaur, and Riuttikjaure. The specified lakes in the groups defined by cluster analysis are believed to be similar in terms of the natural conditions of BS chemistry formation. A large number of lakes not belonging to any of the three groups shows the large diversity of these conditions, which is reflected by a considerable range of background concentrations in BS of the lakes under study.

Fig.2. Cluster analysis dendrogram of the chemical composition of BS in the water bodies under study.

It was also established that the average background concentrations of elements in BS of the lakes under study are similar to average concentrations of chemical elements in the crust of earth (percentage abundance) and in the rocks and soils according to estimation of different researchers (Tables 4 and 5). The calculations by A.P. Vinogradov (1962) show the closest match with the percentage abundance in the bedrocks and soils.

Table 4. Data on average concentration of chemical elements in the crust of earth (µg/g) according to estimates of different researchers (Alexeenko, 2000)

| Researchers | Ni | Cu | Co | Zn | Cd | Pb | As | Hg |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| F. Clark and G. Washington | 180 | 100 | 100 | 40 | 0.10 | 20 | 1.0 | 0.100 |
| A.P. Vinogradov | 58 | 47 | 18 | 83 | 0.13 | 16 | 1.7 | 0.083 |
| S.R. Tailor | 75 | 55 | 25 | 70 | 0.20 | 12.5 | 1.8 | 0.080 |
| A.A. Beus | 95 | 65 | 34 | 87 | 0.19 | 9 | 1.9 | 0.046 |

Table 5. Data on average concentration of chemical elements (µg/g) in the rocks and soils (Alexeenko, 2000)

| Type of rock and soil | Ni | Cu | Co | Zn | Cd | Pb | As | Hg |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Ultrabasic rocks | 20 | 10 | 150 | 50 | 0.10 | 1 | 1.0 | 0.010 |
| Basic rocks | 130 | 87 | 48 | 105 | 0.22 | 6 | 2.0 | 0.090 |
| Medium rocks | 4 | 5 | 1 | 130 | 0.13 | 12 | 1.4 | 0.010 |
| Acidic soils rich in Ca | 15 | 30 | 7 | 60 | 0.13 | 15 | 1.9 | 0.080 |
| Acidic soils poor in Ca | 4.5 | 10 | 1 | 39 | 0.13 | 19 | 1.5 | 0.080 |
| Slates | 68 | 45 | 19 | 95 | 0.30 | 20 | 13.0 | 0.400 |
| Slates+clays | 95 | 57 | 20 | 80 | 0.30 | 20 | 6.6 | 0.400 |
| Sandstone | 2 | 1 | 0.3 | 15 | 0.10 | 7 | 1.0 | 0.030 |
| Carbonates | 20 | 4 | 0.1 | 20 | 0.035 | 9 | 1.0 | 0.040 |
| Soils (A.P. Vinogradov) | 40 | 20 | 8 | 50 | 0.50 | 10 | 5.0 | 0.010 |

Changes of elements concentration in BS in time

The study of chemical composition of the BS column allows reconstructing the history of their formation conditions for particular lakes based on determination of background values of different elements concentration in BS and changes in their incoming during a long period of time. They become especially important when the sedimention rate is known which allows reconstructing the chronology of the system transformation processes.

In assessment of the catchment basins’ regional pollution history, in the framework of international projects paleolimnological method was used (Norton et al., 1992, 1996; Rognerud et al., 1993) and radiometric (age determination according to 210Pb chronology using dating models CRS and CIC) dating of the columns sample (Appleby, Oldfield, 1978). Based on the BS dating results, the sedimentation rates were determined, as well as the sedimented material flow and accumulation of specific elements in the BS. 210Pb chronology may be relied upon only within 150 years because this isotop’s half-life is 22 years. The BS age was extrapolated further in time based on the sedimentation rate in 1850-1900, and thus was accurately determined. The average rate of sedimentation in the latest hundred and fifty years in the lakes was fairly stable within 0.3-0.6 mm/year except for two Finnish lakes Nitsijarvi and Pahtajarvi where these values on an average amount to 1.0 and 1.25 mm/year, respectively.

Earlier research (Dauvalter, 1999; Dauvalter et al., 2012) inverse proportion was noted: the sedimentation increases where the depth of the lake decreases. This is associated with morphometrical peculiarities of lakes: usually, small lakes are less deep, and, consequently, the ration of the lake area and its catchment increases.

Increased concentrations and sedimentation rates of Ni, Cu, and Co in the BS dated back to XX century were observed in the Norwegian lakes (Norton et al., 1992, 1996; Rognerud et al., 1993). Higher concentrations of Pb in the BS, generally, are not related to the Pechenganikel smelters’ emissions. The increase in Pb concentrations dates back to the time too early to be related to any industrial activities in this area. Data based on BS in South Sweden’s lakes confirms Pb atmospheric pollution resulting from its intensive production and use in Europe beginning from the time of Ancient Greek and Roman civilizations (Renberg et al., 1994). It has been noticed that atmospheric deposition of Pb increased as compared to the background values over 2,600 years ago (at a depth of BS 1.5 to 4 meters). Slight but noticeable increase of Pb deposition took place ca. 2,000 years ago; still more significant increase began ca. 1,000 years ago; sedimentation accelerated in XIX, and, especially, in XX century. The accumulation reached its maximum in the 1970’s. Before the industrialization in XIX, concentration of Pb in South Sweden’s lakes BS had already increased due to atmospheric depositions 10-30 times compared to the background level. The background concentrations of Pb (at a depth of BS over 1 meter) in 19 Swedish lakes were found within 2-15 µg/g (dry weight), were usually less than 10 µg/g (Renberg et al., 1994). These values coincide with our investigation of background values.

In North America the rate of Pb accumulation in lakes’ BS gradually increased from 1850-1875 to 1975, and then it has been decreasing until the present time (Norton et al., 1990). In Europe the increase was similar to that described above, but a dramatic increase began 50-75 years earlier. Antropogenic origin of Pb may have numerous sources including smelting, glass factories, and use of tetraethyl Pb as addition to petrol. Cessation of use of the latter resulted in Pb deposition amount decrease in North America. Increase of Pb concentrations may be associated with cross-border Pb transport from its source in North America and southern areas of Europe. Absolute values of Pb accumulation rates are lower in northern areas than those in Southern Norway (Norton, Hess, 1980) or in the south of North America (Norton et al., 1990). A slight increase in Pb concentrations in BS in East Finnmark, Norway is found due to a relatively low BS accumulation rate in the both lakes and very low Pb background concentrations.

Ni, Cu, Co and other HM’s are delivered into the atmosphere with the emissions from the Pechenganikel integrated plant. This is clear from the studies of water and terrestrial ecosystems of the region (Traaen et al., 1990; Rognerud, 1990; Cariat et al., 1996a, 1996b; Dauvalter, 1992, 1994, 1998b; 2003; Dauvalter, Rognerud, 2001; Gregurek et al., 1999; Lukin et al., 2003; Moiseenko et al., 1995; Reimann et al., 1999; Rognerud, Fjeld, 1993; Rognerud et al., 1993, 1998; Äjräs et al., 1995, 1997). Growth of the concentrations and rates of accumulation dates back one decade prior to the beginning of the industrial activities at the Pechenganikel integrated plant. The growth was usually detected in the BS, dated the 1920s and 1930s. This phenomenon has three explanations. First, regional pollution with Co, Cu and Ni possibly existed as a result of the activity of metallurgical plants in the industrial areas of Russia. Until 1940, the Pechenga area was the territory of Finland, where mining resources were already beginning to be explored. Second, the HM’s from the water layer of lakes can settle and redistribute in the BS, which date back prior to introduction of anthropogenic loads. Such diagenetic processes were already described for Zn (Carignan, Tessier, 1985) and other HM. And, third, in the BS dated the 1920s-1930s, the content of organic substance grows (in Lake Dalvatn the values of PPP grow from 29 to 38%, in Lake Durvatn – from 27 to 30%), which is an essential reason for increase of HM adsorption by sediments (Norton et al., 1992). Synchrony of the increase of HM concentrations towards the surface in the BS of isolated lakes, having similar geochemical nature, probably indicates that it is the atmospheric depositions rather than specific catchment processes that are the reason of higher accumulation of HM’s.

Development of the Pechenga copper-and-nickel deposits started in 1932 by the joint Canadian-Finnish company (after Russian October Revolution the territory of today’s Pechenga area joined Finland). The Pechenganikel integrated plant has been operating since 1946, when local sulfide-nickel ore processing resumed in Nikel settlement. In 1959 the production and processing of the ores of the Zhdanovsky deposit started at the plant in Zapoliarny settlement. The composition of emissions from the integrated plant includes sulfur dioxide gas, Ni, Сu, dust, as well as nitrogen oxides and carbon oxide from boiler houses (Kryuchkov, Makarova, 1989). Starting 1971 the processing of high-sulfur (content of S reaches 30%) Cu-Ni ore from Norilsk Mining and Metallurgical Combine hs been performed there. In 1973 204 thousand tons of SO2 were emitted into the atmosphere, in 1979 – 399 t, in 1983 – 293 t. Emissions of Ni were: 1973 – 143 t, 1979 – 438 t, 1983 – 278 t, 1984 – 410 t, 1989 – 512 t, i.e. the maximum emissions of key pollutants, including HM, were recorded in the 80s of the XXth century. Air currents in the atmospheric boundary layer (up to 1,500 m) carry emissions from copper-and-nickel integrated plants long distances from west to east, i.e. not in the direction of neigbouring westerns states (Kryuchkov, Makarova, 1989), therefore, it is the effluent streams from the Pechenganikel integrated plant and not the atmospheric emmissions that is the main source of pollution with Ni, Cu, Co and other HM’s, emitted by the integrated plant, of Lake Kuetsjärvi and downstream the Pasvik River.

To study the anthropogenic load intensity, including the emissions from the Pechenganikel integrated plant, the research was conducted at various periods at the lake catchment area of vertical distribution of HM concentrations in the BS of the lakes under study, located at different distances from smelter shops.

The most polluted with one of the priority HM pollutant – Cu – are the Russian lakes (Pikkujarvi, Shuonijaur), located closer to the emission source of this metal (the Pechenganikel integrated plant), as well as all studied Norwegian lakes of Jarfjord, exposed to intensive atmospheric pollution with the emissions from the smelter shops of the integrated plant (Fig.3). The vertical distribution of Cu in the BS of these lakes testifies of the prevailing role of atmospheric emissions from the Pechenganikel integrated plant in their pollution. Growth of Cu content in the surface layers of BS was also recorded in lakes Ila-Nautsijarvi and Virtuovoshjaur, located 80 and 90 km from the smelter shops respectively. All Finnish lakes and the remaining Russian lakes did not show any pollution of the surface layers of BS.

The data of bio- and chemostratigraphical analysis of the BS of smaller lakes is used for evaluation of long-term changes, occuring in the catchment area of the Pasvik river-and-lake system. Paleoecologic research and reconstruction of the history of the development of aquatic ecosystems is impossible without correct assessment of sedimentation rates, which allows determining the age of the studied BS. The analysis of the radionuclides content and the calculation of mean sedimentation rates were performed at the Institute of Geochemistry and Analytical Chemistry named after V.I.Vernadsky (GEOCHI, RAS). Determination of the activity of radionuclides 137Cs and 210Pb in the bottom sediment samples was performed with the gamma spectrometry nondestructive method using low-background gamma spectrometer Canberra Industries with a solid-state detector based on extra-pure germanium with active diameter 70 mm and thickness 25 mm. The calculated values of absolute sedimentation rates of the studied water bodies are presented in Table 6.

Table 6. Calculated values of absolute sedimentation rates of the studied water bodies

| Lake | Sedimentation rate, cm/year | Approximate age of BS column, years |
| --- | --- | --- |
| Kochejaur | 0.15 | 106 |
| Virtuovoshjaur | 0.07 | 257 |
| Shuonijaur | 0.07 | 210 |
| Ala-Nautsijarvi | 0.16 | 106 |
| Harrijarvi | 0.13 | 240 |
| Rabbvatnet | 0.065 | 687 |

Growth of Cu content in BS columns was recorded in the 70s-80s of the last century in the Russian lakes, located both near the integrated plant (Shuonijaur) and at a distance of about 100 km (Virtuovoshjaur, Kochejaur). The most interesting results were obtained from the long column from Norwegian lake Rabbvatnet – the first noticeable growth of Cu content was observed in the middle of the 17th century, which is probably associated with the beginning of the industrial revolution in the European countries, increase of HM emissions into the environment and their air transport in the direction of the Arctic (Fig.4).

Fig.3. Vertical distribution of Cu concentrations (µg/g of dry weight) in the BS of the lakes under study. In this and in further figures the Finnish lakes are colored in blue, the Russian lakes – in red, the Norwegian lakes - in green.

The next noticeable growth of Cu content was observed in the 19th century, especially in its second half, which may be attributed to the industrialization in Europe, including the European part of Russia. Since then the Cu concentration has kept growing and the intensive growth of Cu content is associated with the beginning of copper-and-nickel production in the Pechenga area (in 1930s), as well as with the beginning of Bjornevatn iron-ore deposit development (in the beginning of the 20th century). Rapid growth of Cu content in the 70s-80s of the 20th century is caused by the beginning of Norilsk ore processing and by the intensive growth of copper-and-nickel production. In the last two decades the production dropped after the collapse of the USSR, but the concentrations of Cu in the BS of Lake Rabbvatnet (as well as in Russian lakes Shuonijaur, Virtuovoshjaur, Kochejaur) have only been growing, which is explained by HM accumulation in the catchment territory of the lakes (Dauvalter et al., 2012).

Fig.4. Vertical distribution of Cu concentrations (µg/g of dry weight) in the dated BS of the lakes under study.

Atmospheric aerosol depositions are the key reason of pollution, including HM, of land and aquatic ecosystems, surface and underground waters (Yakhnin et al., 1997). In the background territories, where the significant role in the balance of atmospheric depositions belongs to the soluble forms of metals, up to 5% of lead deliveries and about 30% of zinc and cadmium deliveries are carried with with the surface washout (Elpatyevsky, 1993; Kabata-Pendias, Pendias, 1989). In the conditions of technogenic pollution, when the role of solid depositions significantly grows, the surface washout decreases to 1-3% of lead delivery and to 10% of zinc and copper delivery (Elpatyevsky, 1993). The remaining part of metals accumulates in soil. Migration of metals in the soil profile runs at speed 0.1-0.4 cm/year and is characterized by rapid drop of concentrations with growth of depth (Elpatyevsky, 1993; Sayet et al., 1990; Cernic et al., 1994). Possibilities of self-cleaning of soils from anthropogenic accumulations of metals are considered as rather limited (Fridland et al., 1992; De Vries, Banker, 1996; Miller, Fridland, 1994). According to the above research, the total washout of metals in the temperate zone (surface run-off, soil solutions, biological processes, etc.), provided that there are no new deliveries from anthropogenic sources, will ensure the self-cleaning of polluted soils from lead over the period from 150-200 up to 400-500 years, from zinc, cadmium over 100-200 years. So, the period of natural self-cleaning of soils and terrestrial ecosystems from metal pollutants can be evaluated by the value equal to n · 102 years (i.e. hundreds of years).

In the Russian lakes (Pikkujarvi, Shuonijaur), located closer to the emission source (Pechenganikel integrated plant), the growth of Ni concentrations is observed in the surface layers of BS (Fig.5), just like the earlier described growth of Cu concentrations. All studied Norwegian lakes of Jarfjord, exposed to intensive atmospheric pollution with the emissions from the smelter shops of the integrated plant, show the growth of Ni content in the surface layers of BS. The growth of Ni content in the top 2 cm of BS was also recorded in other Russian lakes Riuttikjaure and Virtuovoshjaur, located at 90 km from the smelter shops. Unlike Cu, in all Finnish lakes, including Sierramjärvi (over 130 km from the integrated plant), the growth of Ni content is observed in the top 2-3 cm of the BS.

The growth of Ni (as well as Cu) content in the BS columns was recorded in the 70s-80s of the last century in Russian lakes (Fig.6), located both near the integrated plant (Shuonijaur) and at the distance of 90 km away from it (Virtuovoshjaur). Noticeable growth of Ni content in the long column of the BS from Norwegian lake Rabbvatnet dates back to the17th century, which is probably associated (just like in the Cu case) with the beginning of the industrial revolution in the European countries, growth of HM emissions into the environment and their air migration in the direction of the Arctic (Fig.6). The following growth of Ni content dates back to the middle of the 19th century, which may be attributed to the industrialization in Europe, including the European part of Russia. Since then the concentrations of Ni have been gradually growing. The intensive growth of Ni content in the beginning of the 20th century is associated with the development of copper-and-nickel deposits in the Pechenga area and of the Bjornevatn iron-ore deposit in Sør Varanger, however in the middle of the 20th century practically a double drop of Ni content occurs during the termination of production in the years of World War II.

Fig.5. Vertical distribution of Ni concentrations (µg/g of dry weight) in the BS of the lakes under study.

The beginning of Norilsk ore processing and the intensive growth of copper-and-nickel production at the Pechenganikel integrated plant caused a rapid growth of Ni content in the 70s-80s of the 20th century. In the last two decades the production has dropped after the collapse of the USSR, but the Ni concentrations in the BS of Lake Rabbvatnet (as well as in Russian lakes Shuonijaur, Virtuovoshjaur) has only kept growing, which is explained by HM accumulation in the catchment territory of the lakes (Dauvalter et al., 2012).

Fig.6. Vertical distribution of Ni concentrations (µg/g of dry weight) in the dated BS of the lakes under study.

In the vertical distribution of Zn content in the BS of the lakes under study no increase of concentrations has been noted in the surface layers (Fig.7), except for lake Pikkujarvi, located close to the Pechenganikel integrated plant (5 km to the west). Also an insignificant growth of Zn concentrations was recorded towards the BS surface in lakes Virtuovoshjaur (since the beginning of the 20th century, Fig.8) and Gardsjøen, as well as in the near-surface layer of 1-2 cm of Lake Riuttikjaure.

Fig.7. Vertical distribution of Zn concentrations (µg/g of dry weight) in the BS of the lakes under study.

In the majority of the lakes under study there is a tendency to reduction of Zn content towards the BS surface. Probably it is associated with the geochemical peculiarities of this HM, such as rather high migration mobility, its sensitive response to changing physical and chemical conditions in the water body and in the catchment area of the lakes (first of all, the reduction of pH value and showing acidification), higher (versus other HM) need of living organisms in this metal, etc.

Fig.8. Vertical distribution of Zn concentrations (µg/g of dry weight) in the dated BS of the lakes under study.

In the dated BS column of Lake Rabbvatnet, located 30 km in the direction of the prevalent direction of winds, a period of double reduction of Zn content is clearly seen from the middle of the 19th century until the middle of the 20th century (Fig.8), after which the Zn concentrations grew to maximum values in the 1980s (in time this period coincides with maximum production of HM at the Pechenganikel integrated plant), and then towards the BS surface the Zn concentrations drop again, presumably due to the reduction of HM production.

Fig.9. Vertical distribution of Cd concentrations (µg/g of dry weight) in the BS of the lakes under study.

Chalcophylic high-toxic HM Cd in the last decades is considered by many ecologists as a global pollution element (for example, Pacyna, Pacyna, 2001). In the BS depth of the majority of the lakes under study there is a tendency to Cd content growth towards their surface (Fig.9). At the same time the reduction of Cd content occurs in the very top layer of BS (1 to 5 cm) in more than half of the lakes. This fact was recorded in Finnish and Norwegian lakes, as well as in Russian lakes the most distant from the metallurgical production. In lakes Pikkujarvi, Ila-Nautsijarvi and Durvatn a gradual growth of Cd concentrations occurs, and maximum contents are noted in the surface layer (Fig.9).

Fig.10. Vertical distribution of Cd concentrations (µg/g of dry weight) in the dated BS of the lakes under study.

Significant growth of Cd concentrations in the dated BS of the lakes under study was recorded in the beginning of the 20th century (Fig.10). Especially noticeable was the growth of Cd content in the middle of last century, and it was associated with the intensive industrial development in general after World War II (in the lakes located one hundred kilometers away from the main source of pollution, which is the Pechenganikel integrated plant, – Kochejaur and Virtuovoshjaur), and with the resumption of metallurgical production at the integrated plant (in the lakes located in the air emission exposure zone, – Rabbvatnet). Cd content reduction in the surface layer of the dated BS was recorded in all the lakes under study and is dated to one-two decades, which may be associated with the reduction of HM production after the collapse of the USSR or with the reduction of global emission of Cd over the last decades.

Chalcophylic high-toxic HM Pb, just like Cd, in the last decades is considered by many ecologists as a global pollution element (for example, Pacyna, Pacyna, 2001). In the BS depth of all the lakes under study without exceptions the growth of Pb content is noted towards their surface (Fig.11), regardless whether the lakes are located near the point sources of pollution or at a significant distance from them. At the same time in the very top layer of BS (1 to 3 cm) in half of the lakes the reduction of Pb content occurs. This fact was recorded in Finnish and Norwegian lakes, as well as in Russian lakes the most distant from the metallurgical production. In other half of the lakes the Pb concentrations gradually grow and maximum contents are noted in the surface layer (Fig.11).

Noticeable growth of Pb concentrations in the dated BS of Lake Rabbvatnet was recorded in the beginning of the 18th century (Fig.12), which may be associated with the development of the industrial revolution in the European countries. Since then the Pb content has been continuously growing due to the enhancement of metallurgical production, including Pb. Especially noticeable growth of Pb content in the BS of all dated lakes occurred in the middle of last century, and it is associated with the intensive industrial development in general after World War II, including the ever growing use of leaded petrol and with the resumption of the metallurgical production at the integrated plant. The reduction of Pb content in the surface layer of BS was recorded in the majority of the lakes under study and is dated to one-two decades, which may be associated with the reduction of HM production after the collapse of the USSR and with the reduction of global emission of Pb in the latest decades. Possibly, the main reason of Pb content reduction in the latest decades is the prohibition to use leaded petrol, first in the European countries, and then in Russia.

Fig.11. Vertical distribution of Pb concentrations (µg/g of dry weight) in the BS of the lakes under study.

Fig.12. Vertical distribution of Pb concentrations (µg/g of dry weight) in the dated BS of the lakes under study.

The following chalcophylic high-toxic HM As, just like Cd and Pb, in the last decades is considered by many ecologists as a global pollution element (for example, Pacyna, Pacyna, 2001). In the BS depth of the majority of the lakes under study the growth of As content is noted towards their surface (Fig.13), with the exception of two lakes, Harrijärvi and Toartesjaur. The maximum As contents were recorded in the surface layer of BS columns of the majority of lakes – of all Norwegian lakes, Russian lakes, located closer to the integrated plant, as well as Finnish lakes Sierramjärvi and Lampi 222. At the same time in the very top layer of BS (from 1 to 3 cm) of four lakes, as a rule, more distant from point sources of pollution (Pechenganikel integrated plant), reduction of As content occurs (Fig.13), which is suggestive of the consequences of the global emission reduction of this chalcophylic element, very hazardous for the environment.

Fig.13. Vertical distribution of As concentrations (µg/g of dry weight) in the BS of the lakes under study.

Noticeable growth of As concentrations in the dated BS of Lake Rabbvatnet was recorded in the beginning of the 19th century (Fig.14), which may be associated with the development of the industrial revolution in the European countries. Untill this time the continuous reduction of As content was recorded from the deepest BS layers, beginning from the 14th century.

Fig.14. Vertical distribution of As concentrations (µg/g of dry weight) in the dated BS of the lakes under study.

During the 19th and the 20th centuries the content of As has been continuously growing due to the enhancement of industrial production, including As. Especially noticeable growth of As content in the BS of all dated lakes occurred in the middle of last century, and it is associated with the intensive industrial development in general after World War II, including the ever growing use of As in the metallurgy industry, including the resumption of metallurgical production at the integrated plant. The reduction of As content in the BS surface layer of some studied lakes is dated to one-two decades, which may be associated with the reduction of metallurgical production after the collapse of the USSR or with the reduction of the global emission of As in the latest decades. Possibly, the reason for the reduction of As content in the latest decades is the prohibition to use it in the European countries, including Russia, for medical purposes, mainly in dentistry.

Fig.15. Vertical distribution of Hg concentrations (µg/g of dry weight) in the BS of the lakes under study.

Another chalcophylic element is a highly toxic HM Hg, which, just like Cd, Pb and As, in the latest decades is considered by many ecologists as a global pollution element (for example, Pacyna, Pacyna, 2001). In the BS depth of the majority of the lakes under study, except for Lake Toartesjaur, the growth of Hg sediments is noted towards their surface (Fig.15). Maximum contents of Hg were recorded in the surface layer of the BS columns of the majority of the lakes – of all Norwegian lakes, of Russian lakes Kochejaur and Ila-Nautsijarvi, located closer to the integrated plant, and also Finnish lakes Harrijärvi and Lampi 222. At the same time the reduction of Hg content occurs in the very top layer of the BS (from 1 to 3 cm) of six lakes (Fig.15), which can be suggestive of the consequences of the reduction of the global emission of this chalcophylic element, very hazardous to the environment.

Noticeable growth of Hg concentrations in the dated BS of Lake Rabbvatnet was recorded, just like as As, in the beginning of the 19th century (Fig.16), which may be associated with the development of the industrial revolution in the European countries. Untill that time a rather consistent content of Hg was recorded (0.06-0.08 µg/g), with some increase in the end of the 15th century. During the 19th and the 20th centuries the consistent growth of content occurs due to the inhancement of industrial production, including Hg, due to utilization of Hg compounds for various purposes – in medicine, in engineering, in agriculture for the production of pesticides. Especially noticeable growth of Hg content in the BS of all dated lakes occurred in the middle of last century, and it is associated with the intensive industrial development in general after World War II, including the ever growing fuel combustion, and first of all of coal, which contains high concentrations of Hg, in metallurgy, including the resumption of metallurgical production at the Pechenganikel integrated plant. Reduction of Hg content in the surface layer of the BS of some lakes under study is dated to on-two decades, which may be associated with the reduction of metallurgical production after the collapse of the USSR and with the reduction of the global emission of Hg in the latest decades due to understanding of high hazard of this metal. Possibly the reason for the reduction of Hg content in the latest decades is the recycling of household appliances, first of all, of mercury-containing, fluorescent and other lamps.

Fig.16. Vertical distribution of Hg concentrations (µg/g of dry weight) in the dated BS of the lakes under study.

In the vertical distribution of Co content in the BS of the lakes under study the growth of concentrations was found in the surface layers of all Norwegian lakes (Fig.17), as well as of the Russian lakes located close to the Pechenganikel integrated plant (Pikkujarvi and Shuonijaur). Also a significant growth of Co concentrations was recorded in the layer of 6-7 cm of the BS of Finnish lake Lampi 222, which is the closest to the integrated plant among all the Finnish lakes. Other studied lakes show the tendency of Co content reduction towards the BS surface.

In the dated BS column of the Norwegian lake Rabbvatnet located 30 km in the direction of the prevalent direction of winds, a period of Co content reduction is clearly noted by the beginning of the 20th century (Fig.18), after which the Co concentrations continuously kept growing until they reached maximum values in the beginning of the 21st century, and then Co concentrations again drop towards the BS surface, probably due to the reduction of HM production. The growth of Co content in Lake Shuonijaur dates back to the 1970s, when processing of Norilsk ore started at the integrated plant. Sumultaneous growth of Co content was also recorded in the BS of Lake Virtuovoshjaur.

Fig.17. Vertical distribution of Co concentrations (µg/g of dry weight) in the BS of the lakes under study.

Fig.18. Vertical distribution of Co concentrations (µg/g of dry weight) in the dated BS of the lakes under study.

# Territorial distribution of elements in the surface bottom sediments

Long-term anthropogenic load on the catchment areas of the lakes has led to alteration of natural conditions of the formation of BS chemical composition and to growth of HM concentrations in the surface BS layers in comparison to background contents (Table 7).

Table 7. HM concentrations (в µg/g of dry weight) in the surface layer (0-1 cm) of BS, background values and the values of factors (Cf) and degree (Cd) of the pollution of the lakes under study

| Lakes | Layer | LOI | Cu | Ni | Zn | Co | Cd | Pb | As | Hg | Cd |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Lampi 222 | 0-1 | 28.08 | 134 | 74 | 80 | 31.7 | 0.53 | 44 | 7.7 | 0.382 |  |
|  | 29-30 | 31.30 | 200 | 21 | 145 | 11.3 | 0.54 | 7 | 1.9 | 0.318 |  |
|  | Cf |  | 0.7 | 3.5 | 0.6 | 2.8 | 1.0 | 6.3 | 4.0 | 1.2 | 20.0 |
| Harrijärvi | 0-1 | 40.16 | 21.9 | 40.0 | 62.5 | 1.34 | 0.41 | 26.9 | 2.54 | 0.094 |  |
|  | 29-30 | 24.24 | 24.3 | 15.8 | 123 | 4.44 | 0.20 | 6.92 | 1.66 | 0.046 |  |
|  | Cf |  | 0.9 | 2.5 | 0.5 | 0.3 | 2.0 | 3.9 | 1.5 | 2.0 | 13.7 |
| Pitkä- | 0-1 | 23.83 | 62.4 | 77.1 | 88.6 | 43.1 | 0.31 | 23.5 | 9.08 | 0.156 |  |
| Surnujärvi | 29-30 | 17.91 | 64.0 | 20.0 | 98.4 | 9.44 | 0.45 | 4.36 | 1.76 | 0.068 |  |
|  | Cf |  | 1.0 | 3.9 | 0.9 | 4.6 | 0.7 | 5.4 | 5.2 | 2.3 | 23.8 |
| Sierramjärvi | 0-1 | 21.94 | 16.1 | 42.3 | 77.3 | 8.62 | 0.19 | 26.2 | 17.3 | 0.074 |  |
|  | 29-30 | 18.51 | 17.6 | 25.7 | 83.1 | 6.50 | 0.25 | 4.84 | 1.80 | 0.032 |  |
|  | Cf |  | 0.9 | 1.6 | 0.9 | 1.3 | 0.8 | 5.4 | 9.6 | 2.3 | 22.9 |
| Shuonijaur | 0-1 | 48.23 | 59.5 | 90.9 | 40.9 | 9.60 | 0.12 | 12.1 | 3.42 | 0.084 |  |
|  | 15-16 | 33.03 | 22.5 | 27.3 | 72.7 | 7.40 | 0.16 | 2.76 | 1.59 | 0.06 |  |
|  | Cf |  | 2.6 | 3.3 | 0.6 | 1.3 | 0.7 | 4.4 | 2.2 | 1.3 | 16.4 |
| Ala- | 0-1 | 31.82 | 28.8 | 40.0 | 170 | 30.0 | 0.79 | 27.9 | 11.9 | 0.316 |  |
| Nautsijarvi | 24-25 | 27.24 | 57.5 | 75.0 | 254 | 42.9 | 1.06 | 12.5 | 4.58 | 0.18 |  |
|  | Cf |  | 0.5 | 0.5 | 0.7 | 0.7 | 0.7 | 2.2 | 2.6 | 1.8 | 9.7 |
| Ila- | 0-1 | 39.06 | 29.6 | 37.7 | 106 | 7.22 | 0.41 | 18.6 | 3.18 | 0.144 |  |
| Nautsijarvi | 14-15 | 29.32 | 17.5 | 34.7 | 169 | 12.6 | 0.29 | 2.26 | 2.62 | 0.048 |  |
|  | Cf |  | 1.7 | 1.1 | 0.6 | 0.6 | 1.4 | 8.2 | 1.2 | 3.0 | 17.9 |
| Pikkujarvi | 0-1 | 17.9 | 327 | 511.6 | 130 | 31.1 | 0.27 | 12.7 | 10.4 | 0.114 |  |
|  | 13-14 | 20.8 | 59.3 | 78.4 | 95.8 | 11.3 | 0.13 | 5.82 | 2.60 | 0.056 |  |
|  | Cf |  | 5.5 | 6.5 | 1.4 | 2.7 | 2.0 | 2.2 | 4.0 | 2.0 | 26.4 |
| Toartesjaur | 0-1 | 37.42 | 12.7 | 18.4 | 50.3 | 4.60 | 0.15 | 9.64 | 1.70 | 0.018 |  |
|  | 22-23 | 30.21 | 12.8 | 19.2 | 62.9 | 7.64 | 0.11 | 1.50 | 1.60 | 0.042 |  |
|  | Cf |  | 1.0 | 1.0 | 0.8 | 0.6 | 1.4 | 6.4 | 1.1 | 0.4 | 12.6 |
| Virtu- | 0-1 | 39.68 | 27.7 | 45.5 | 109.1 | 16.7 | 0.56 | 28.6 | 4.52 | 0.212 |  |
| ovoshjaur | 14-15 | 52.51 | 14.4 | 36.4 | 100.0 | 13.9 | 0.23 | 8.16 | 2.12 | 0.09 |  |
|  | Cf |  | 1.9 | 1.3 | 1.1 | 1.2 | 2.4 | 3.5 | 2.1 | 2.4 | 15.9 |
| Riuttikjaure | 0-1 | 29.6 | 17.5 | 59.2 | 98.6 | 5.40 | 0.51 | 19.2 | 1.44 | 0.072 |  |
|  | 16-17 | 25.1 | 15.2 | 28.9 | 89.5 | 4.86 | 0.19 | 3.06 | 1.42 | 0.010 |  |
|  | Cf |  | 1.2 | 2.0 | 1.1 | 1.1 | 2.7 | 6.3 | 1.0 | 7.2 | 22.6 |
| Kochejaur | 0-1 | 47.8 | 16.4 | 27.3 | 81.8 | 7.00 | 0.43 | 19.3 | 2.44 | 0.166 |  |
|  | 17-18 | 37.8 | 17.5 | 27.3 | 100.0 | 11.2 | 0.17 | 3.66 | 1.68 | 0.09 |  |
|  | Cf |  | 0.9 | 1.0 | 0.8 | 0.6 | 2.5 | 5.3 | 1.5 | 1.8 | 14.5 |
| Gardsjøen | 0-1 | 42.26 | 217 | 221 | 97.3 | 46.2 | 0.44 | 39.0 | 24.8 | 0.354 |  |
|  | Ref | 34.85 | 69.0 | 40.6 | 86.5 | 14.5 | 0.47 | 3.60 | 5.40 | 0.108 |  |
|  | Cf |  | 3.1 | 5.4 | 1.1 | 3.2 | 0.9 | 10.8 | 4.6 | 3.3 | 32.5 |
| Holmvatnet | 0-1 | 36.26 | 170 | 184 | 138 | 139 | 0.83 | 64.4 | 10.3 | 0.208 |  |
|  | Ref | 23.92 | 79.3 | 40.6 | 178 | 30.6 | 0.82 | 26.1 | 3.8 | 0.100 |  |
|  | Cf |  | 2.1 | 4.5 | 0.8 | 4.5 | 1.0 | 2.5 | 2.7 | 2.1 | 20.3 |
| Rabbvatnet | 0-1 | 43.55 | 315 | 247 | 100 | 11.0 | 0.57 | 43.9 | 4.90 | 0.354 |  |
|  | 42-43 | 32.40 | 75.9 | 23.6 | 106 | 4.78 | 0.21 | 3.08 | 3.06 | 0.078 |  |
|  | Cf |  | 4.1 | 10.4 | 0.9 | 2.3 | 2.8 | 14.3 | 1.6 | 4.5 | 41.0 |
| Durvatn | 0-1 | 60.81 | 499 | 594 | 76.5 | 118 | 1.03 | 38.3 | 34.2 | 0.514 |  |
|  | Ref | 31.15 | 31.0 | 21.9 | 58.8 | 30.0 | 0.34 | 2.94 | 5.12 | 0.062 |  |
|  | Cf |  | 16.1 | 27.2 | 1.3 | 3.9 | 3.1 | 13.0 | 6.7 | 8.3 | 79.5 |

The content of elements in the BS depends on many factors: grain-size composition of sediments, depth of the lake, geochemical condition in the water depth and in the BS (mainly pH and Eh), the sedimentation rate of suspended particles, content of organic material, fine organic and mineral particles in the water of the water body, concentration of oxides and hydroxides of Fe and Mn in the BS, etc. (Håkanson, Jansson, 1983; Horowitz, 1991; Rognerud et al., 1993; Dauvalter, 2000). The studied lakes are characterized by rather large depths, neutral values of pH from 6.4 to 7.3, rather low alkalinity (average of 150 mcg-equ/l). All these factors are favorable for accumulation of HM’s in the BS (Håkanson, Jansson, 1983). But the main reason of high concentrations of HM pollutants (first of all Ni, Cu, Co) in the surface layers of BS are the atmospheric emissions from the smelter shops of the Pechenganikel integrated plant, especially near the integrated plant.

The surface layers of BS reflect the accumulative effect of aero-industrial load of metals on the catchment areas, which often cannot be recorded by hydrochemical methods. Dust emissions into the atmosphere from the smelter shops of the Pechenganikel integrated plant are the major source of high concentrations of Ni, Сu and Со (10-180 times more than the background values) in the surface layers of BS at the distance up to 30-40 km (Dauvalter, 1994). These elements have a close positive correlation, which testifies of a single anthropogenic source of their delivery and of similar ways of migration.

The majority of HM’s included into the composition of the emissions and waste water from industrial plants are tied and stay in the BS. The previous studies (Moiseenko et al., 1996; Moiseenko et al., 1995; Dauvalter, 1995, 1997, 1998, 2000, 2002; Dauvalter, 1992, 1994, 1997 et al.) established that the dust emissions into the atmosphere from the Pechenganikel integrated plant and the wastewater from the smelter shops, mud disposal sites, slurry ponds and mines are the main sources of high concentrations of Ni, Cu, Co, Cd, Zn, As and Hg in the surface layers of the BS in the lakes of the Pechenga area.

The highest concentrations of Ni, Cu and Co, exceeding background values by 5-25 times, were noted in the lakes at a distance up to 40-50 km from the integrated plant (Fig.19). Significant reduction of concentrations to 1-3 background values is observed at a distance over 50 km from the source of pollution.

A similar pattern is observed in the distribution of Cd, As, and Hg. The same area up to 50 km is polluted most intensively (Fig.19). There the exceedance of metals concentrations over the background values is noted from 2 to 8 times. When a distance of 50 km from the integrated plant is reached, it is noted that the concentrations of metals are reduced to 1-3 of the background values. However, in some lakes located at a significant distance high concentrations of As and Hg are also noted (for example, in lakes Sierramjärvi and Riuttikjaure, respectively).

Fig.19. Distribution of the concentrations of key pollution elements (µg/g) in the surface layer (0-1 cm) of the BS of the lakes under study depending on the distance from the Pechenganikel integrated plant.

The contents of Zn in the BS surface insignificantly (up to 1.4 times in Lake Pikkujarvi) exceed the background values; therefore this element can be referred to nonpollution elements.

In the distribution of Pb according to the results of our studies no tendency of content growth in the surface layers of BS was noted with the approach to the integrated plant (Fig.19), which testifies of the fact that MMC “Pechenganikel” is not the major source of pollution with Pb, i.e. the picure is different from all the priority pollutant HM’s. Earlier (Dauvalter, 1997, 2000; Dauvalter, 1997; Dauvalter, Rognerud, 2001) a picture different from all HM’s was noted in the regional distribution of Pb – increase of concentrations from east to west. The largest values of Pb concentrations were recorded in the Norwegian territory (just like in this study), where mean concentrations are 40 µg/g, which is ca. 10 background values. In the industrial area the reduction of concentrations is now recorded (mean concentrations are 12 µg/g or 2-4 background values).

A similar picture of distribution of Ni and Cu concentrations in the surface of the BS of the lakes is also noted around the world’s largest copper-and-nickel integrated plants – the Norilsk integrated plant in Siberia and Sudbury plant in Canada (Fig.20). Concentrations of Ni and Cu in the surface BS of the lakes around the Norilsk integrated plant are within the range from 37 to 2,142 and from 63 to 5,400 µg/g respectively (Blais et al., 1998), lowering as the distance from the smelters increases. Exceedance over background values reaches 28. The greatest exceedance was noted at a distance less than 20 km from the integrated plant. The same reduction is also observed around Sudbury, where impact of the emissions from the copper-and-nickel integrated plant on Ni and Cu concentrations in the surface BS of the lakes is limited to 30-40 km (Bradley, Morris, 1986; Palmer et al., 1989; Semkin, Kramer, 1976; Nriagu et al., 1982), whereas the impact zone around the Norilsk integrated plant sperads to 60 km (Blais et al., 1998). Spacial distribution of Ni and Cu has a north-east – south-west elliptical shape with the center in Sudbury (Controy et al., 1975; Semkin, Kramer, 1976). A similar trend with Ni and Cu was noted for atmospheric precipitations and for geochemistry of the lakes, including water pH (Controy et al., 1975; Reimann et al., 1999). Therefore, the distribution of Ni and Cu in the surface BS of the lakes in the Murmansk Region around Norilsk and Sudbury fully coincides, just like the distribution of these elements in atmospheric precipitations (Kryuchkov, Makarova, 1989) and in the water of the lakes (Moiseenko et al., 1996, Moiseenko et al., 1995).

The most polluted are the lakes, located in the immediate proximity of the Pechenganikel integrated plant. These are: Lake Pikkujarvi located at the distance of 4 km from the source of pollution, as well as Lake Shuonijaur and all Norwegian lakes in the 20-40 km zone and receiving the most of the emissions from the integrated plant and characterized by maximum concentrations of Ni, Cu, As and Hg, as well as Pb in the surface layers of BS. Further away at 60-100 km from the integrated plant the reduction of concentrations is noted, first of all of Ni and Cu, but the pollution with chalcophylic elements (especially Pb) remains quite serious.

Fig.20. Concentration of Ni (а) and Cu (b) in the surface BS of the lakes (in µg/g of dry weight), depending on the distance from the smelter shops of Kola MMC (dots – our data), the Norilsk integrated plant (Blais et al., 1998) and Sudbury, Canada (Bradley, Morris, 1986).

Fig.21. Distribution of the concentrations of elements (µg/g) in the surface layer (0-1 cm) of BS and the pollution degree value (Cd) of the lakes under study, depending on the distance from the Pechenganikel integrated plant.

A very close relationship between the content of alkaline and alkaline-earth metals (first of all K, Na and Mg) in the BS surface and the distance from the source of pollution was noted – concentrations grow closer to the Pechenganikel integrated plant (Fig.21). This means that along with the emissions of heavy metals the integrated plant also releases into the atmosphere the alkaline and alkaline-earth metals, which are included into ore-hosting and stripping rocks, containing minerals with large content of these elements.

To determine the factors that have the largest impact on the formation of chemical composition of the BS of the lakes in the conditions of anthropogenic load of various intensity, factor analysis was performed (Table 8), which clearly identified the first factor, having the greatest weight (29%) and uniting the priority pollution HM’s (Ni and Cu), which main sources of delivery into the environment in the studied region are the emissions from the Pechenganikel integrated plant. These elements demonstrate clear dependence of content reduction in the surface layers of BS on the distance from the source of pollution, which manifests itself in the high factor at “Distance” parameter. In this factor the alkaline and alkaline-earth metals (K, Na, Mg) and Al also have high coefficients. It confirms our conclusion that along with the emissions of heavy metals the integrated plant also emits into the atmosphere the alkaline and alkaline-earth metals and Al, which was mentioned earlier. The high coefficient of the “masl” (meters above sea level) parameter in the factor model also draws attention to itself, which means that the height of the water level in the lake above sea level greatly influences the formation of the chemical composition of the modern BS. Chalcophylic elements (Cd, Pb, As, Hg), having the status of global pollution elements, are clearly prominent in the 2nd factor (factor weight is 23%), which confirms the previous conjecture that the sources of the delivery of these extremely toxic elements along with the emissions from the Pechenganikel integrated plant can be others, and they can be located far from the lakes under study. Pb and Hg are also emitted by the integrated plant, but there are other sources of their delivery into water bodies – they are the global pollution of the atmosphere of the Northern hemisphere, use of Hg in household appliances (mercury lamps, etc.). The main source of Pb delivery into the environment is fuel (liquid and solid) combustion in power plants and the delivery of this metal occurs practically everywhere, including the vehicle exhaust gases and other internal combustion engines, boiler houses, etc. Natural factors and parameters, such as LOI, Mn, Zn, are prominent in the third factor (factor weight 13%), as well Fe and P, having rather high coefficients in the factor model. The content of Fe and Mn, as well as P, depends on physical and chemical conditions in the water body (first of all on oxidation-reduction potential and pH value, on the biological activity, on the manifestations of acidification processes, on eutrophication, which was mentioned above). Behaviour of Zn can also be associated with the peculiarities of geochemical conditions. Zinc, despite its release by the integrated plant, is characterized by rather good dilution and its intensive use by hydrobionts, therefore, in its distribution no clear dependence on the distance from the source of pollution is detected.

Table 8. Factor model of the chemical composition of the surface BS of the lakes under study. The most significant parameters with factors over 0.7 are typed in bold type.

|  | Factor 1 | Factor 2 | Factor 3 |
| --- | --- | --- | --- |
| Catchment | 0.210 | -0.084 | 0.324 |
| area | 0.206 | -0.304 | -0.042 |
| masl | 0.664 | 0.192 | -0.192 |
| Distance | 0.715 | -0.200 | 0.221 |
| H2O | 0.391 | 0.250 | -0.412 |
| LOI | 0.186 | 0.387 | -0.714 |
| Cu | -0.707 | 0.548 | -0.365 |
| Ni | -0.795 | 0.410 | -0.291 |
| Zn | -0.372 | 0.334 | 0.710 |
| Cd | -0.104 | 0.874 | 0.002 |
| Pb | -0.111 | 0.748 | 0.011 |
| As | -0.251 | 0.736 | -0.102 |
| Hg | -0.188 | 0.860 | -0.179 |
| Mn | 0.086 | 0.425 | 0.783 |
| Fe | 0.172 | 0.314 | 0.551 |
| P | 0.141 | 0.565 | 0.618 |
| K | -0.913 | -0.324 | 0.153 |
| Nа | -0.926 | -0.254 | 0.015 |
| Ca | -0.669 | -0.517 | -0.042 |
| Mg | -0.936 | -0.309 | 0.103 |
| Co | -0.332 | 0.756 | -0.016 |
| Sr | -0.239 | -0.189 | -0.162 |
| Al | -0.862 | -0.179 | 0.176 |
| Factor weight, % | 28.7 | 23.2 | 13.2 |

Cluster analysis (Fig.22) clearly identified three groups of water bodies: first – lakes Harrijärvi, Ila-Nautsijarvi and Virtuovoshjaur, which are characterized by relatively small contents of priority pollutant HM (Ni, Cu), second – lakes Shuonijaur and Rabbvatnet with relatively high concentrations of Ni and Cu and other HM’s, and third – closely located Russian lakes Toartesjaur, Riuttikjaure and Kochejaur, located far from the Pechenganikel integrated plant at the distance over 80 km and characterized by relatively small contents of priority pollutant HM’s (Ni, Cu), as well as other HM’s, except for Pb and Hg in Lake Riuttikjaure. Probably the mentioned lakes in the groups, identified by the cluster analysis, are similar by natural and anthropogenic conditions of the formation of chemical composition of the BS. A large number of lakes, not included into any of the groups, suggest a great variety of these conditions, which reflected itself in the significant range of the contents of the elements in the BS surface of the lakes under study.

Fig.22. Dendrogram of the cluster analysis of the chemical composition in the surface layer (0-1 cm) of the BS of the lakes under study.

Therefore, it was established that dust emissions into the atmosphere from the Pechenganikel integrated plant and waste water from smelter shops, mud disposal sites, slurry ponds and mines are the main sources of high concentrations of Ni, Cu, Со, as well as Cd, As and Hg in the surface layers of the BS of the lakes, located up to 40-50 km from the integrated plant (Fig.19). High concentrations of Cd, Рb, Hg and As in the surface layers are also noted in the lakes, located far from the Pechenganikel integrated plant (Fig.19), for example, in Russian lakes Kochejaur, Virtuovoshjaur, Riuttikjaure, Toartesjaur et al., as well as in all Finnish lakes. At the same time dependence is established of the concentrations reduction in the surface layers of the BS of the lakes of the north-west of the Murmansk Region for the studied chalcophylic elements (As and Hg) on the distance from the main source of pollution, which suggests that the emissions from smelter shops are the source of pollution with these elements, high-toxic in high concentrations, besides the priority pollutants – Ni, Cu and Co. Maximum mean concentrations in the surface BS layers of Cd, Рb, As and Hg are noted in Norwegian lakes. Growth of alkaline and alkaline-earth metals (first of all K, Na and Mg) was also noted in the BS surface of the lakes, located near the Pechenganikel integrated plant, which testifies of the fact that the integrated plant is the source of these metals in the composition of dust emissions.

# Factor and degree of pollution

To assess the geoecological condition of the surface waters we chose the method of determining the factor and degree of pollution, proposed by Swedish scientist L. Håkanson (Håkanson, 1980), and adapted to the conditions of the European Subarctic with the consideration of the identified patterns of the formation of the chemical composition of BS, background contents of the elements in the BS. The pollution factor (Cfi) was calculated as the quotient from the division of the element or compound concentration in the surface centimeter layer by the background value, set in the deepest part of the BS column. The pollution degree (Cd) was determined as the sum of the pollution factors for all pollution substances.

The following classification was adhered to in this approach Cfi: Cfi<1 – low; 1(Cfi<3 – moderate; 3(Cfi<6 – significant; Cfi(6 – high pollution factor. Likewise, in characterizing the pollution degree, made up by the pollution factors of separate elements, the classification was followed based on the summation of the pollution factors for 8 elements (Ni, Cu, Co, Zn, Cd, Pb, As, Hg): Cd<8 – low; 8(Cd<16 – moderate; 16(Cd<32 – significant; Cd(32 – high pollution degree, testifying of serious pollution (Håkanson, 1980).

According to the research results very high values of Cd were noted in Norwegian lakes at a distance up to 40 km from the sources of pollution, and significant values – up to 60 km (Table 7, Fig.21), besides, the lakes, located in the prevalent direction of the prevailing winds (to the north-west from the integrated plants), have larger Cd values. The largest input into the Cd value of the lakes, located up to 40 km, is made by the metals, emitted into the atmosphere by the Pechenganikel integrated plant in large quantities (first of all Ni and Cu), and in the more distant lakes the main pollution elements are becoming the chalcophylic elements Pb, Hg and As, which over the last decades have obtained the status of the global pollution elements.

The largest values of the pollution factor (Cf) were noted for Ni and Cu (27 and 16 respectively) in Norwegian lake Durvatn, located 30 km from the integrated plant. Similar pattern was noted for Co in Norwegian Lake Holmvatnet, the largest value of the pollution factor is smaller (4.5), and it refers to the “significant” group. The largest Cf value for Cd (3.1 – ‘significant’ according to the classification of Håkanson) was noted in Lake Durvatn. The largest Cf values for Pb were also noted in Norwegian lakes Rabbvatnet and Durvatn (14.3 and 13.0, respectively). Maximum Cf values for As and Hg were recorded in lakes Sierramjärvi and Durvatn, respectively (9.6 and 8.3). All the above-mentioned values of the pollution factors for Pb, As and Hg refer to “high” according to the classification of Håkanson. In general, there was a pattern noted, that high pollution factors for Ni and Cu are observed near the integrated plant, and for chalcophylic Pb, As and Hg they are also recorded at a significant distance from the integrated plant (Table 7), which confirms the conclusions redarding the global nature of pollution with these high-toxic elements, including Russian and Finnish water bodies.

# Conclusion

To study the ecological condition of the water bodies of the border territory between Russia, Norway and Finland, the columns of bottom sediments (BS) were sampled from 16 lakes: 4 Finnish lakes, 8 Russian lakes and 4 Norwegian lakes. Research of BS was performed at the lakes located in the impact zone of the emissions from the Pechenganikel integrated plant and exposed to anthropogenic load of different intensity.

The research was performed to evaluate the accumulation and distribution of elements, including HM’s, in the BS of the water bodies. Four aspects were reviewed in the study of the BS: 1) background contents, 2) vertical distribution of elements, 3) concentrations in the surface layers of BS, 4) determination of anthropogenic load intensity by the values of the factor and the degree of pollution, caused by the HM’s, accumulated in the BS.

It was established that the largest background concentrations of HM’s in BS were noted in different lakes: Cu and Hg in Lake Lampi 222, Zn and Cd in Lake Ala-Nautsijarvi, Co in Lake Ila-Nautsijarvi, Ni in Lake Pikkujarvi, Pb in Lake Holmvatnet, As in Lake Gardsjøen, which is caused by geochemical (for example, availability of the deposits of mineral resources) and morphometric peculiarities of the catchment territory and of the lake itself. Generally, mean background concentrations of the studied HM in the BS of the lakes under study are similar to mean background concentrations in the water bodies of the north-west of Murmansk Region, calculated earlier (Kashulin et al. 2009). Exceptions are chalcophylic elements Cd, Pb and Hg, which background contents in the BS of the lakes under study are twice as high, and As twice as low than the ones that were established earlier.

Mean sedimentation rates in the lakes under study are rather consistent and are in the limits of 0.7-1.6 mm/year. Maximum sedimentation rate was noted in Lake Kochejaur. Growth of Ni, Cu and Co content in the BS of the lakes, which have been dated, was normally noted in the layers, which age dates back to the 1920s and 1930s, and maximum values are reached in the 1970s-1980s, as a result of metallurgical activities in this region. The greater the distance from the Pechenganikel integrated plant, the smaller the concentrations of Ni and Cu in the surface layers of BS and the smaller the scatter of contents for the column, in general. The most interesting are the results for the long column from Norwegian Lake Rabbvatnet – the first noticeable growth of Ni and Cu content dates back to the middle of the 17th century, which is probably associated with the beginning of the industrial revolution in the European countries, with the growth of HM emissions into the environment and their air migration towards the Arctic. Noticeable growth of Pb concentrationbs in the dated BS of Lake Rabbvatnet was recorded in the beginning of the 18th century. With growth of distance from the Pechenganikel integrated plant, Pb becomes one of the key pollutants. Especially this is characteristic of the Finnish lakes. Noticeable growth of Pb content in the BS of all dated lakes occurred in the middle of last century, and it is associated with the intensive industrial development in general after World War II, including the ever growing use of leaded petrol and with the resumption of metallurgical production at the integrated plant. Reduction of Pb content in the BS surface was recorded in the majority of the lakes under study and is dated to one-two latest decades. Pollution markers for catchment areas are also Hg, As and Cd, the beginning of the pollution with these elements dates back to the beginning/ middle of the 19th century.

Dust emissions into the atmosphere from the smelter shops of the Pechenganikel integrated plant are the major source of high concentrations of Ni, Сu and Со (5-25 times more than the background values) in the surface layers of BS at the distance up to 40-50 km. Significant reduction of concentrations to 1-3 of the background values is observed at the distance over 50 km from the source of pollution. Similar pattern is observed in the distribution of Cd, As, and Hg. The area up to 50 km is the most intensively polluted. The exceedence of metals concentrations over the background values by 2 to 8 times is noted there. At a distance of 50 km from the integrated plant the metals concentrations are reduced to 1-3 of the background values. In the distribution of Pb, according to the results of our research, no tendency was noted for content growth in the surface layers of BS as we approach the integrated plant, which testifies of the fact that MMC “Pechenganikel” is not the main source of pollution with Pb. The greatest values of Pb concentrations were recorded in the Norwegian territory, where mean concentrations are 40 µg/g, which equals ca. 10 background values. Reduction of concentrations was recorded in the industrial area (mean concentrations 12 µg/g or 2-4 of the background values). A very close relationship was noted between the content of alkaline and alkaline-earth metals (first of all K, Na and Mg) in the BS surface and the distance from the source of pollution – concentrations grow as we get closer to the Pechenganikel integrated plant.

According to the research results very high values of pollution degree (Cd) were noted in Norwegian lakes at a distance up to 40 km from the sources of pollution, and significant values – up to 60 km, besides, the lakes located in the windprevailing directions (to the north-west from the integrated plants), have larger Cd values. The largest input into the Cd value of the lakes, located up to 40 km, is made by the metals, released into the atmosphere by the Pechenganikel integrated plant in large quantities (first of all Ni and Cu), and in the more distant lakes the main pollution elements are becoming the chalcophylic elements Pb, Hg and As, which in the latest decades have obtained the status of the global pollution elements.

Therefore, as a result of the research of the chemical composition of the BS of the lakes of the north-west of the Murmansk Region and of the border areas of Norway and Finland a tendency was established of the enhancement of anthropogenic load on the catchment areas of the lakes and on the lakes themselves despite the reduction of emissions and waste water with pollutants from the Pechenganikel integrated plant over the latest 20 years. Mean emissions of Ni and Cu from the integrated plant amounted to 300 and 200 t/year respectively, and wastewater - to 5 and 0.2 t/year. Over the 70-year period of the activity of the Pechenganikel integrated plant an enormous quantity of HM has accumulated in the environmental components (mainly in terrestrial ecosystems – in soils and plants), which after dying of plants and decomposition of organic residue with the slope run-off, soil and underground waters in the form of organic and inorganic compounds is gradually delivered into watercourses and water bodies. With the consideration of the accumulated HM in terrestrial ecosystems and of the long-term period of their self-cleaning, intensive delivery of HM into the water bodies will continue for many decades, even if their emissions into the environment are greatly reduced.

# References

V.A.Alexeenko Ecological geochemistry. М.: Logos, 2000. p.627.

Large lakes of the Kola Peninsula / K.G. Kupetskaya, I.I. Velikoretskaya, B.G. Venus et al. L.: Science, 1976. p.349.

Yu.A. Bogdanov Pelagic deposition process in the Pacific Ocean: synopsis of a thesis … Dr. Sci. in Geology and Mineralogy. М., 1980. p.44.

V.F.Brekhovskikh. Hydrophysical factors of the development of oxygen regimen in water bodies. М: Science, 1988. p.168.

V.F.Brekhovskikh., G.N.Vishnevskaya, D.V.Lomova, E.R.Shakirova Regarding the role of bottom sediments in the balance of dissolved oxygen in the Mozhaisk water reservoir // Water resources. 1998а. V. 25, No.1. p. 43-45.

V.F.Brekhovskikh, Z.V.Volkova, G.N.Vishnevskaya Alteration of the elements of ecosystems in submerged quarries for aggregates production // Water resources. 1998б. V. 25, No.4. p. 448-454.

E.V.Venitsianov Some peculiarities of heavy metals sorption by the layer of bottom sediments and soils // Water resources. 1998. V. 25, No.4. p. 462-466.

E.V.Venitsianov, R.N.Rubinstein Dynamics of the sorption of liquid media. М.: Science, 1983. 238 p.

V.I.Vernadsky Selected works. М.: ASUSSR, 1954.

A.P.Vinogradov Average content of chemical elements in the main types of volcanic rock of Earth crust // Geochemistry. 1962. No.7. p. 555-571.

T.A.Vlasova Hydrochemistry of the main riveers. Syktyvkar: Komi SC Ural Div. of RAS, 1988. p.150.

V.A.Dauvalter Concentrations of heavy metals in the bottom sediments of the lakes of the Kola Peninsula as the pollution indicator of aquatic ecosystems // Problems of chemical and biological monitoring of the ecological condition of water bodies of the Kola North. Apatity: Published by KSC of RAS, 1995. p. 24-35.

V.A.Dauvalter Pollution of bottom sediments of the Pasvik River catchment with heavy metals // Geoecology. 1997. No.6. p. 43-53.

V.A.Dauvalter Heavy metals in the bottom sediments of the river-and-lake system “Lake Inari – the Pasvik River” // Water resources. 1998. V. 25, No.4. p. 494-500.

V.A.Dauvalter Patterns of sedimentation in the water bodies of the European Subarctic (environmental aspects of the problem): synopsis of a thesis … Dr. of Geogr. Sciences. Apatity: Published by KSC of RAS, 1999. p.52.

V.A.Dauvalter Chemical composition of bottom sediments of the subsrctic lake, impacted by mining metallurgy // Izvestiya of AS. Geographical series. 2002, No.4. p. 65-73.

V.A.Dauvalter, N.A.Kashulin, S.S.Sandimirov Tendencies of alterations of the chemical composition of bottom sediments of freshwater Subarctic and Arctic water bodies, impacted by natural and anthropogenic factors // Works by the Kola SC of RAS. Applied Ecology of the North. Release 1. – 2012. – No.2 (9). – p. 54-87.

A.I.Denisova, E.P.Nakhshina, B.I.Novikiv, А.К.Ryabov Bottom sediments of water reservoirs and their impact on water quality. Kiev, Naukova dumka, 1987. p.162.

A.V.Evseev, Т.М.Krasovskaya Ecological geographical peculiarities of natural environment of the regions of the Russian Extreme North. Smolensk: Published by the SSU, 1996. p.232.

P.V.Elpatyevsky Geochemistry of migration flows in natural technogenic systems. М.: Science, 1993. p.253.

O.S.Zvereva Peculiarities of the biology of the main rivers of Komi ASSR. L.: Science, 1969. p.275.

А.Kabata-Pendias, H.Pendias Microelements in soils and plants. М.: Mir, 1989. p.439.

N.A.Kashulin, V.A.Dauvalter, T.G.Kashulinа, S.S.Sandimirov, N.E.Ratkin, L.P.Kudryavtseva, I.M.Korolyova, O.I.Vandysh, O.I.Mokrotovarova Anthropogenic changes of the running aquatic ecosystems of the Murmansk Region. Part 1: Kovdor District. Apatity: Published by KSC of RAS, 2005. p.234.

N.A.Kashulin, V.A.Dauvalter, S.S.Sandimirov, N.E.Ratkin, P.M.Terentyev, I.M.Korolyova, O.I.Vandysh, L.P.Kudryavtseva Anthropogenic changes of the running aquatic ecosystems of the Murmansk Region. Part 2: Lake-river system of the Chuna River in the conditions of aerotechnogenic pollution. Apatity: Published by KSC of RAS, 2007. p.238.

N.A.Kashulin, D.B.Denisov, S.S.Sandimirov, V.A.Dauvalter, T.G.Kashulinа, D.N.Malinovsky, O.I.Vandysh, B.P.Ilyashuk, L.P.Kudryavtseva Anthropogenic changes of water systems of the Khibini mountain group (the Murmansk Region). Apatity: Published by KSC of RAS, 2008. V. 1. p.250. V. 2. p.282.

N.A.Kashulin, S.S.Sandimirov, V.A.Dauvalter, P.M.Terentyev, D.B.Denisov Ecological catalogue of the lakes of the Murmansk Region. North-western part of the Murmansk Region and of the territory of the border with neigbouring countries. Apatity: Published by KSC of RAS, 2009. P. I. p.226. P. II. p.262.

N.A.Kashulin, S.S.Sandimirov, V.A.Dauvalter, L.P.Kudryavtseva, P.M.Terentyev, D.B.Denisov, S.A.Valkova Annotated ecological catalogue of the lakes of the Murmansk Region (Eastern part. Catchment of the Barents Sea). In 2 p. Apatity: Published by KSC of RAS, 2010. P. 1, p.249, P. 2, p.128.

V.V.Kryuchkov, T.D.Makarova Aerotechnogenic impact on the ecosystems of the Kola North. Apatity: Published by KSC, 1989. p.96.

P.N.Linnik, B.I.Nabivanets Forms of metals migration in fresh surface waters. L.: Gidrometeoizdat, 1986. p.270.

P.N.Linnik, Т.А.Vasilchuk, Yu.B.Nabivanets Exchange of organic substances and compounds of metals in the system “Bottom sediments – water” in the conditions of simulation experiment // Ecological chemistry. 1997. V. 6, No.4. p. 217-225.

A.P.Lisitsin Processes of ocean sedimentation. М., 1978. p.392.

A.A.Lukin, V.A.Dauvalter, N.A.Kashulin, N.E.Ratkin Impact of aerotechnogenic pollution on the catchment area of the Subarctic lakes and fish // Ecology. 1998. No.2., p.109-115.

A.A.Lukin, V.A.Dauvalter, A.P.Novosyolov The ecosystem of the Pechora River in modern conditions. Apatity: Published by KSC of RAS, 2000. p.192.

T.I.Moiseenko Theoretical basis for rationing of anthropogenic loads on Subsrctic water bodies. Apatity: Published by KSC, 1997. p.261.

T.I.Moiseenko, I.V.Rodyushkin, V.A.Dauvalter, L.P.Kudryavtseva Development of water quality and bottom sediments in the conditions of anthropogenic loads on the water bodies of the Arctic Basin (with the example of the Kola North). Apatity: Published by KSC of RAS, 1996. p.263.

T.I.Moiseenko, V.A.Dauvalter, I.V.Rodyushkin Geochemical migration of elements in the subarctic water body (with the example of Lake Imandra). Apatity: Published by KSC, 1997. p.127.

T.I.Moiseenko, V.A.Dauvalter, I.V.Rodyushkin Mechanisms of natural and anthropogenic metals turnover in the surface waters of the Subarctic // Water resources. 1998. V. 25, No.2. p. 231-243.

T.I.Moiseenko, V.A.Dauvalter, A.A.Lukin, L.P.Kudryavtseva, B.P.Ilyashuk, Е.А. Ilyashuk, S.S.Sandimirov, L.Ya.Kagan, O.I.Vandysh, A.N.Sharov, Yu.N.Sharova, I.M.Korolyova (Edited by T.I.Moiseenko) Anthropogenic modifications of the ecosystem of Lake Imandra. М: Science, 2002. p. 487.

J.V.Moor, S.Ramamurti Heavy metals in natural waters. М.: Mir, 1987. p.285.

А.М.Nikanorov, A.V.Zhulodov Biomonitoring of metals in freshaquatic ecosystems. L.: Gidrometeoizdat, 1991. p.312.

Lakes of various landscapes of the north-west of the USSR. L.: Science, P. I. and II, 1974.

Yu.E.Sayet, B.A.Revich, E.P.Yanin et al. Environmental geochemistry. М.: Nedra, 1990. p.335.

N.I.Semenovich Bottom sediments of Lake Ladoga. М.-L.: Science, 1966. p.124.

N.I.Semenovich Bottom sediments of Lake Onega. L.: Science, 1973. p.104.

L.V.Sergeeva Geochemical characteristics of some lake landscapes of the north-west // Lakes of various landscapes of the north-west of the USSR. P. I. L.: Science, 1968. p.34-58.

L.V.Sergeeva Migration of the group of microelements in two different landscapes of the Kola Peninsula // Lakes of various landscapes of the Kola Peninsula. P. I. L.: Science, 1974. p. 50-77.

N.M.Strakhov, N.G.Brodskaya, L.M.Knyazeva, A.N.Razzhivina, М.А.Rateev, D.G.Sapozhnikov, E.S.Shishova, Development of sediments in modern water bodies. М.: Published by ASUSSR, 1954. p.792.

E.I.Fyodorova Summary of iron-ore lakes of the Kola Pewninsula // Substance accumulation in lakes. М., Science, 1964. p.59-77.

А.Е.Fersman Selected works. М.: ASUSSR, 1953-1959. V.1-5.

Yu.P.Hrustalyov Sedimentogenesis in intracontinental seas of arid zone: synopsis of a thesis … Dr. of Geol.-Mineral. Sciences. М., 1986. p.51.

E.Ya.Yakhnin, O.V.Tomilina, D.A.Delarov Atmospheric depositions of heavy metals and their impact on ecological condition of soils // Ecological chemistry. 1997. No.6(4). p. 253-259.

Abry T., Skogheim O.K., Hongve D. Sedimentene i Tyrifjorden. Tungmetaller og dateringer. Tyrifjordundersokelsen // Fagrapport nr. 19. 1982. 19 p.

Appleby P.G., Oldfield F. The calculation of the 210Pb dates assuming a constant rate of supply of unsupported 210Pb to sediments // Catena. 1978. V. 5. P. 1-8.

Blais J.M., Duff K.E., Laing T.E., Smol J.P. Regional contamination in lakes from the Noril'sk region in Siberia, Russia // Water, Air, Soil Pollut. 1998. V. 95. P. 1-16.

Bradley R.W., Morris J.R. Heavy metals in fish from a series of metal-contaminated lakes near Sudbery, Ontario // Water, Air, Soil Pollut. 1986. V. 27. P. 341-357.

Cariat P. de, Reimann C., Äjräs M., Niskavaara H., Chekushin V.A., Pavlov V.A. Stream water geochemistry form selected catchments on the western Kola Peninsula (NW Russia) and neighbouring areas of Finland and Norway: 1. Element levels and sources // Appl. Geochem. 1996a. V. 2. P. 149-168.

Cariat P. de, Reimann C., Äjräs M., Niskavaara H., Chekushin V.A., Pavlov V.A. Stream water geochemistry form selected catchments on the western Kola Peninsula (NW Russia) and neighbouring areas of Finland and Norway: 2. Time-series // Appl. Geochem. 1996b. V. 2. P. 169-184.

Carignan R., Tessier A. Zinc deposition in acid lakes: the role of diffusion // Science. 1985. V. 228. P. 1524-1526.

Cernic M., Federer P., Borcovec M., Sticher H. Modeling of heavy metal transport in a contaminated soil // J. Environ. Qual. 1994. V. 23. P. 1239-1248.

Controy N., Hawley K., Keller W., LaFrance C. Influence of the atmosphere on lakes in the Sudbury area // International Association of Great Lakes Research. Proc. Symp. Atmospheric Contribution to the Chemistry of Lake Waters, Sept. 28-Oct. 1, 1975.

Dauvalter V. Concentrations of heavy metals in superficial lake sediments of Pechenga district, Murmansk region, Russia // Vatten. 1992. V. 48, No.2. P. 141-145.

Dauvalter V. Heavy metals in lake sediments of the Kola peninsula, Russia // Sci. Tot. Environ. 1994. V. 158. P. 51-61.

Dauvalter V. Heavy metal concentrations in lake sediments as an index of freshaquatic ecosystem pollution // Crawford R.M.M. (ed.) Disturbance and recovery in Arctic lands; an ecological perspective. Kluwer Academic Publishers, Dordrecht, the Netherlands, 1997. P. 333-351.

Dauvalter V.A. Heavy metals in the bottom sediments of the Inari-Pasvik river-and-lake system // Water Resources. 1998. V. 25, No.4. P. 451-457.

Dauvalter V. Impact of mining and refining on the distribution and accumulation of nickel and other heavy metals in sediments of subarctic lake Kuetsjärvi, Murmansk region, Russia // J. Environ. Monitor. 2003. V. 5 (2). P.210-215.

Dauvalter V., Rognerud S. Heavy metals pollution in sediment of the Pasvik River drainage // Chemosphere. 2001. V. 42, No 1. P. 9-18.

Dauvalter V., Sandimirov S. Pollution of the Sediments of the Paz River basin / Eds. Stebel K., Chritinsen G., Derome J., Crekela I. State of the environment in the Norwegian, Finnish and Russian border area. The Finnish Environment. 2007. No.6. 55 p.

Dauvalter V., Kashulin N., Sandimirov S., Terentjev P., Denisov D. Amundsen P.-A. Chemical composition of lake sediments along a pollution gradient in a Subarctic watercourse // J. Environ. Sci. Health. A. 2011 (in press).

De Vries W., Banker D.J. Manual for calculating critical load of heavy metals for soils and surface water. DLO Winland Staring Centre, Wageningen (The Neterlands). Report No 114, 1996. 133 p.

Douglas E.R. Sources of mercury contamination in the sediments of small headwater lakes in south-central Ontario, Canada // Arch. Environ. Contam. Toxicol. 1986. V. 15. P. 505-512.

Förstner U., Wittmann G.T.W. Metal Pollution in the Aquatic Environment. Berlin: Springer-Verlag, 1979. 210 p.

Förstner U., Wittmann G.T.W. Metal Pollution in the Aquatic Environment. N.Y.: Springer-Verlag, 2nd revised edition, 1981. 486 p.

Fridland A.J., Craig B.M., Miller E.K., Herrick G.T., Siccama T.G., Johnson A.N. Decreasing lead levels in the forest floor of the northeastern USA // AMBIO. 1992. V. 21. P. 400-430.

Gregurek D., Melcher F., Pavlov V.A., Reimann C., Stumpf E.F. Mineralogy and mineral chemistry of snow filter residues in the vicinity of the nickel-copper processing industry, Kola Peninsula, NW Russia // Miner. Petrol. 1999. V. 65. P. 87-111.

Horowitz A.J. A primer on trace metal-sediment chemistry. Chelsea, Michigan: Lewis Publishers, 2nd rew. ed., 1991. 136 p.

Håkanson L. Sediments as indicator of contamination Investigation in the four largest Swedish lakes. Uppsala: SNN RM 835/ NLU Rapport 92, 1977. 27 p.

Håkanson L. An ecological risk index for aquatic pollution control – a sedimentological approach // Water Res. 1980. V. 14. P. 975-1001.

Håkanson L. Sediment sampling in different aquatic environments: Statistical aspects // Water Resour. Resear. 1984. V. 20, No 1. P. 41-46.

Håkanson L., Jansson M. Principles of lake sedimentology. Berlin: Springer-Verlag, 1983. 316 p.

Johansson K. Heavy metals in Swedish forest lakes - factors influencing the distribution in sediments. Doctoral dissertation. Uppsala University, Sweden, 1988.

Kashulin N.A., Ratkin N.E., Dauvalter V.A., Lukin A.A. Impact of airborne pollution on the drainage area of subarctic lakes and fish // Chemosphere. 2001. V. 42, No 1. P. 51-59.

Kashulin N.A., Dauvalter V.A., Sandimirov S.S., Terentjev P.M., Koroleva I.M. Catalogue of lakes in the Russian, Finnish and Norwegian Border Area. Jyvaskyla, Finland: Kopijyva Oy, 2008. 313 p.

Lukin A., Dauvalter V., Kashulin N., Yakovlev V., Sharov A., Vandysh O. Assessment of copper-and-nickel industry impact on a subarctic lake ecosystem // Sci. Tot. Environ. 2003. V. 306. P. 73-83.

Melnikov S.A. Report on heavy metals // State of the Arctic Environment. Rovaniemi: Arctic Centre Publications, 1991. P. 82-153.

Megar S.A. Polluted precipitation and the geochronology of mercury deposition in lake sediments of Norther Minnesota // Water, Air, Soil Pollut. 1986. V. 30. P. 411-419.

Miller E.K., Fridland A.J. Lead migration in forest soil. Response to changing atmospheric inputs // Environ. Sci. Technol. 1994. V. 28. P. 662-672.

Moiseenko T., Mjelde M., Brandrud T. et al. Pasvik River Watercourse, Barents Region: Pollution Impacts and Ecological Responses. Investigations in 1993. Oslo: NIVA-report OR-3118, 1994. 87 p.

Moiseenko T.I., Kudryavtseva L.P., Rodyushkin I.V., Dauvalter V.A., Lukin A.A. and Kashulin N.A. Airborne contaminants by heavy metals and aluminium in the freshaquatic ecosystems of the Kola subarctic region (Russia) // Sci. Tot. Environ. 1995. V. 160/161. P. 715-727.

Mudroch A., Sarazin L., Lomas T. Summary of surface and background concentrations of selected elements in the Great Lakes sediments // Great Lakes Res. 1988. V. 14, No 2. P. 241-251.

Norton S.A., Hess C.T. Atmospheric deposition in Norway during the last 300 years as recorded in SNSF lake sediments: I. Sediment dating and chemical stratigraphy // Proc. Intern. Ecol. Impact of Acidic Precipitation, SNSF-project, Sandefjorden, Norway, 1980. P. 274-275.

Norton S.A., Dillon P.J., Evans R.D., Mierle G., Kahl J.S. The history of atmospheric deposition of Cd, Hg and Pb in North America: Evidence from lake and peat bog sediments // Lindberg S. E. et al. (Eds.). Sources, Deposition and Capony Interactions. V. III, Acidic Precipitation. New York: Springer-Verlag, 1990. P. 73-101.

Norton S.A., Henriksen A., Appleby P.G. et al. Trace metal pollution in eastern Finnmark, Norway, as evidenced by studies of lake sediments. Oslo: SFT-report 487/92, 1992. 42 p.

Norton S.A., Appleby P.G., Dauvalter V., Traaen T.S. Trace metal pollution in eastern Finnmark, Norway and Kola Peninsula, Northeastern Russia as evidences by studies of lake sediment // NIVA-Report 41/1996, Oslo, 1996. – 18 p.

Nriagu J.O., Wong H.K.T., Coker R.D. Deposition and chemistry of pollutant metals in lakes around the smelter at Sudbary, Ontario // Environ. Sci. Technol. 1982. V. 16. P. 551-560.

Pacyna J.M., Pacyna E.G. An assessment of global and regional emissions of trace elements to the atmosphere from anthropogenic sources worldwide // Environ. Rev. 2001. V. 4. P. 269-298.

Rada R.G., Wiener J.G., Wintrey M.R., Powel D.E. Recent increases in atmospheric deposition of mercury to North Central Wisconsin lakes inferred from sediment analyses // Arch. Environ. Contam. Toxicol. 1989. V. 18. P. 175-181.

Palmer G.R., Dixit S.S., Macarthur J.D., Smol J.P. Elemental analysis of lake sediment from Sudbery, Canada, using particle-induced X-ray emisssion // Sci. Tot. Environ. 1989. V. 87/88. P. 141-156.

Reimann C., Banks D., Bogatyrev I., de Cariat P., Kashulina G., Niskavaara H. Lake water geochemistry on the western Kola Peninsula, north-west Russia // Appl. Geochem. 1999. V. 14. P. 787-805.

Rekolainen S., Verta M., Liehu A. The effect of airborne mercury and peatland drainage on sediment mercury content in some Finnish forest lakes // Helsinki: National Board of Water. 1986. V. 65. P. 11-21.

Renberg I., Persson M.W., Emteryd O. Pre-industrial atmospheric lead contamination detected in Swedish lake sediments // Nature. 1994. V. 368. P. 323-326.

Rognerud S. Kvikksolv i Mjosa's sedimenter. Oslo: NIVA-rapport 0-82105, 1985. 47 p.

Rognerud S. Sedimentundersøkelser i Pasvikela høsten 1989. Oslo: NIVA-Rapport 401/90, 1990. 10 p.

Rognerud S., Norton S.A., Dauvalter V. Heavy metal pollution in lake sediments in the border areas between Russia and Norway. Oslo: NIVA-Report 522/ 93, 1993. 18 p.

Rognerud S., Fjeld E. Regional survey of heavy metals in lake sediments in Norway // AMBIO. 1993. V. 22, No 4. P. 206-212.

Rognerud S., Skotvold T., Fjeld E., Norton S.A., Hobak A. Concentrations of trace elements in recent and preindustrial sediments from Norwegian and Russian Arctic lakes // Can. J. Fish. Aquat. Sci. 1998. Vol. 55. P. 1512-1523.

Semkin R.G., Kramer J.R. Sediment geochemistry of Sudbury area lakes // Can. Mineral. 1976. V. 14. P. 73-90.

Skogheim O.K. Rapport fra Arungenprosjektet. Oslo: As- NLH, Nr. 2, 1979. 7 p.

State of the environment in the Norwegian, Finnish and Russian border area. Eds. Stebel K., Chritinsen G., Derome J., Crekela I. The Finnish Environment, 2007, No.6. 98 p.

Traaen T. S., T. Moiseenko, V. Dauvalter, S. Rognerud, A. Henriksen, L. Kudravseva. Acidification of surface waters, nickel and copper in water and lake sediments in the Russian-Norwegian border areas. Working Group for Water and Environmental Problems under the Norwegian-Soviet Environmental Protection Commission. Oslo and Apatity, 1991. 20 p.

Tenhola M., Lummaa M. Regional distribution of zinc in lake sediments from eastern Finland // Symposium on Economic Geology, Dublin, Ireland, 26-29 August, 1979. P. 67-73.

Äjräs M., Cariat P. de, Chekushin V.A., Niskavaara H., Reimann C. Ecological investigation, Kola Peninsula: sulfur and trace element contents in snow // Water, Air, Soil Pollut. 1995. V. 85. P. 749-754.

Äjräs M., Pavlov V.A., Reimann C. Comparison of sulfur and heavy metal contents and their regional distribution in humus and moss samples from vicinity of Nikel and Zapoljarnij, Kola Peninsula, Russia // Water, Air, Soil Pollut. 1997. V. 98. P. 361-380.

# Text boxes

United distance

Dendrogram for 16 variables

Single connection method

Euclidean distance

Distance from intergrated plants, km

Ni concentration (µg/g) in the surface BS of the lakes

Kola Peninsula

Norilsk

Sudbury, Canada

Distance from intergrated plants, km

Ni concentration (µg/g) in the surface BS of the lakes

Kola Peninsula

Sudbury, Canada

Norilsk

United distance

Dendrogram for 16 variables

Single connection method

Euclidean distance